## Slide 1
Multi-IMU Calibration, Fusion, and Bias Estimation for Improved Odometry
Final Presentation @ Amazon Robotics
August 20th, 2025
Jongwon Lee

## Slide 2
Generating and incorporating a virtual IMU helps!
Code available [GluonImuFusion] [CR]
2025-07-18-15-11-06
2025-07-23-13-59-33
2025-07-18-15-11-06
Translation error in wheel–IMU odometry (/odom_fusion) over nine 1-hour sessions, depending on the IMU(s) used
What the existing Gluon codebase does
What this project improves
IMU | Mean (Stdv.)
TDK | 0.324 (0.397)
Ouster | 0.600 (0.667)
Virtual | 0.292 (0.256)
TDK + Ouster | 0.263 (0.261)
TDK + Ouster + Virtual | 0.239 (0.180)

## Slide 3
IMU measures specific force (by accelerometer) and angular rate (by gyroscope) along three orthogonal axes
IMU is pivotal component of modern mobile robots – including Proteus with various applications (e.g., navigation, anomaly detection)
Introduction – IMU is essential in mobile robots
Xsens IMUs (single-IMU system)
Array of 32 MPU9150 IMUs (multi-IMU system)
A distributed inertial navigation system on a spacecraft
The coordinate frames of the Ouster IMU (left) and TDK IMU (right) on the drive unit. (Red: x, Green: y, Blue: z)

## Slide 4
In reality, IMU measurements deviate from their “true values” (i.e., what we are supposed to measure)
Motivation – Ensuring accurate IMU measurement is important!
Accelerometer measurement:
Gyroscope measurement:
Scale and non-orthogonality matrices
Time-varying biases
White noises
Quantities subject to be estimated and calibrated
Quantities subject to be mitigated (e.g., by filter or sensor fusion)
: Linear acceleration of the IMU frame with respect to the world fame, expressed in the IMU frame
: Angular velocity of the IMU frame with respect to the world fame, expressed in the IMU frame
What we actually measure
What we are supposed to measure
I explored several approaches that would allow us to obtain the “true values”
Spatial and temporal relationships (when multiple IMUs are used)

## Slide 5
Overview
Estimable vs. non-estimable calibration parameters of drive-unit IMUs
Static testing for intrinsic accelerometer calibration
Inter-IMU temporal calibration via time-offset search maximizing gyroscope magnitude correlation
Experiment: Pure IMU odometry before and after calibration
Calibration of IMUs
Multi-IMU fusion for noise & drift reduction
Generating a virtual IMU from TDK and Ouster IMU measurements
Allan variance analysis of the virtual IMU: Does fusion always improve noise and random walk characteristics?
Experiment: Pure IMU odometry using TDK, Ouster, and virtual IMUs
Learning-based IMU bias estimation
Modeling bias evolution (e.g., neural ODE approach)
Experiment: Pure IMU odometry with and without bias compensation estimated via neural ODE
Mutiple-IMU experiments for wheel-IMU odometry
Wheel–IMU odometry with individual IMUs (TDK, Ouster, Virtual)
Wheel–IMU odometry with multiple IMUs

## Slide 6
Where we are at
Estimable vs. non-estimable calibration parameters of drive-unit IMUs
Static testing for intrinsic accelerometer calibration
Inter-IMU temporal calibration via time-offset search maximizing gyroscope magnitude correlation
Experiment: Pure IMU odometry before and after calibration
Calibration of IMUs
Multi-IMU fusion for noise & drift reduction
Learning-based IMU bias estimation
Mutiple-IMU experiments for wheel-IMU odometry
Accelerometer measurement:
Gyroscope measurement:
Spatial and temporal relationships (when using multiple IMUs)

## Slide 7
The estimable calibration parameters on drive units are identified
Estimable vs. non-estimable calibration parameters of drive-unit IMUs
[1] Yang, Geneva, and Huang. “Multi-Visual-Inertial System: Analysis, Calibration and Estimation.” International Journal of Robotics Research, 2024.
[2] Yang, Geneva, Zuo, and Huang. “Online imu intrinsic calibration: Is it necessary?” RSS 2020.
[3] Chen, Li, Li, Zhou, and Yang. “iKalibr: Unified Targetless Spatiotemporal Calibration for Resilient Integrated Inertial Systems.” IEEE Transactions on Robotics, 2025.
[4] Jauffret. “Observability and fisher information matrix in nonlinear regression.” IEEE Trans. Aerosp. Electron. Syst., 2007.
See Multi-IMU Calibration, Fusion, and Bias Estimation for Improved Odometry and IMU calibration — Static test for accelerometer intrinsic parameter estimation
Calibration parameters | Can a drive unit (i.e., a wheeled ground robot) collect the required data? | Reference values
Accelerometer intrinsic | O | Identity
Gyroscope intrinsic | X | Identity
Temporal extrinsic | O | Zero
Spatial extrinsic | X | CAD information (i.e., those in /tf_static)
depend on the system’s motions, which determine parameter observability [1-4]

## Slide 8
Accelerometer intrinsics can be estimated from a set of static data by placing the IMU in multiple orientations
The IMU orientations must cover all the three linearly independent orientations
Using a ramp—even at just a few degrees—allows a drive unit to collect data in non-planar orientations
Static testing for intrinsic accelerometer calibration
Acquiring static data on a planar surface from the drive unit results in failure!
Collect static data in multiple orientations: (1) on a flat plane and (2) on ramps with multiple yaw directions
Estimate , by minimizing the sum of squares of
Calibrate raw accelerometer data with the estimated ,
+ The constant bias in the gyroscope can also be
estimated and calibrated using static data
See IMU calibration — Static test for accelerometer intrinsic parameter estimation

## Slide 9
The constant time offset between multiple IMU timestamps can be estimated by maximizing the correlation of gyroscope magnitudes
This is because any location on the same rigid body experiences the same angular velocity magnitudes
Inter-IMU temporal calibration via time-offset search maximizing gyroscope magnitude correlation
See Interim check-in: Multi-IMU fusion for noise reduction
+ Ground-truth to the IMU can also
be synced in the same way

## Slide 10
Pure IMU odometry was performed before and after calibration of the IMUs on ab216
Experiment: Pure IMU odometry before and after calibration
Calibration helps!
Any results, in what follows, were obtained using calibrated data (unless otherwise specified)
 | Uncalibrated | Calibrated
TDK | 68.7 (16.5) | 11.1 (7.3)
Ouster | 39.1 (9.6) | 4.9 (3.1)
* Aggregated results from 15 sequences across four sessions, with durations of 4-10 min, trajectory lengths of 230-1050 m, and rotations of 1100-3000°
Mean and standard deviation of absolute orientation error (AOE, °) across 15 sequences
 | Uncalibrated | Calibrated
TDK | 253,653.5 (192,948.0) | 12,026.8 (6,156.1)
Ouster | 162,048.0 (124,955.8) | 6,327.2 (6,387.6)
Mean and standard deviation of absolute position error (APE, m) across 15 sequences
matters
, matter

## Slide 11
Where we are at
Calibration of IMUs
Learning-based IMU bias estimation
Mutiple-IMU experiments for wheel-IMU odometry
Accelerometer measurement:
Gyroscope measurement:
Multi-IMU fusion for noise & drift reduction
Generating a virtual IMU from TDK and Ouster IMU measurements
Allan variance analysis of the virtual IMU: Does fusion always improve noise and random walk characteristics?
Experiment: Pure IMU odometry using TDK, Ouster, and virtual IMUs

## Slide 12
The measurement of a virtual IMU is generated by combining data from the TDK and Ouster IMUs
Generating a virtual IMU from TDK and Ouster IMU measurements
[6] Zhang, Xu, Chen, and Li. “A Lightweight and Accurate Localization Algorithm Using Multiple Inertial Measurement Units.” IEEE Robotics and Automation Letters, 2020.
Set an arbitrary frame
,
(where , , with and )
,
where ,
Caveat 1: If two identical IMUs are combined, the noise is reduced by √2 Caveat 2: If two IMUs are of the same grade (i.e., difference < √3), the noise is reduced compared to using a single IMU alone
In what follows, let it be identical to the TDK frame
The coordinate frames of the Ouster IMU (left) and TDK IMU (right) on the drive unit. (Red: x, Green: y, Blue: z)
,
,
TDK
Ouster

## Slide 13
We assess the white noise and random walk characteristics of TDK, Ouster, and virtual IMUs
Allan variance analysis of the virtual IMU: Does fusion always improve noise and random walk characteristics?
A virtual IMU may not necessarily outperform the TDK and Ouster IMUs in both white noise and random walk characteristics
 | TDK | Ouster | Virtual
White noise in gyroscope (Unit: rad/s/√Hz) | 9.22E-05 | 3.38E-04 | 1.84E-04
White noise in accelerometer (Unit: m/s²/√Hz) | 1.59E-03 | 6.47E-03 | 2.01E-03
Random walk in gyroscope (Unit: rad/s·√Hz) | 4.73E-06 | 2.04E-06 | 4.93E-07
Random walk in accelerometer (Unit: m/s²·√Hz) | 0.00E+00 | 0.00E+00 | 0.00E+00
Allan variance analysis of white noise and random walk characteristics for TDK, Ouster, and virtual IMUs on ab216
[8] Cho and Park, “A calibration technique for a redundant imu containing low-grade inertial sensors.” ETRI journal, 2005.
Code available [GluonImuNavTools] [CR]

## Slide 14
Pure IMU odometry was performed on the TDK, Ouster, and virtual IMUs on ab216
Experiment: Pure IMU odometry using TDK, Ouster, and virtual IMUs
The largest error in the TDK IMU is likely due to its higher random walk compared to the Ouster or virtual IMUs
The impact of introducing virtual IMU for wheel-IMU odometry on drive units will be discussed later
TDK | Ouster | Virtual
11.1 (7.3) | 4.9 (3.1) | 7.2 (4.9)
* Aggregated results from 15 sequences across four sessions, with durations of 4-10 min, trajectory lengths of 230-1050 m, and rotations of 1100-3000°
Mean and standard deviation of absolute orientation error (AOE, °) across 15 sequences
Mean and standard deviation of absolute position error (APE, m) across 15 sequences
matters
, matter
TDK | Ouster | Virtual
12,026.8 (6,156.1) | 6,327.2 (6,387.6) | 6,497.9 (3,465.0)

## Slide 15
Where we are at
Calibration of IMUs
Mutiple-IMU experiments for wheel-IMU odometry
Accelerometer measurement:
Gyroscope measurement:
Multi-IMU fusion for noise & drift reduction
Learning-based IMU bias estimation
Modeling bias evolution (e.g., neural ODE approach)
Experiment: Pure IMU odometry with and without bias compensation estimated via neural ODE

## Slide 16
Neural ODE (nODE) aims to learn the evolution of IMU biases by modeling
, ,
thereby allowing the estimation of their time-varying behavior
We explored the feasibility of nODE for estimating IMU biases of the drive units
Modeling bias evolution (e.g., neural ODE approach)
[7] Liu, Lin, Zhang, and Ghaffari. “Debiasing 6-DOF IMU via Hierarchical Learning of Continuous Bias Dynamics.” RSS 2025.
9 layers, 28K parameters
11 layers, 210K parameters
Cost functions:

## Slide 17
Pure IMU odometry was conducted on the TDK, Ouster, and virtual IMUs for ab216, (1) without and (2) with compensating the time-varying bias estimated by nODE
Experiment: Pure IMU odometry with and without bias compensation estimated via neural ODE
nODE does not reduce errors in IMU odometry for the drive units, leaving room for future work
 | Without nODE | With nODE
TDK | 11.1 (7.3) | 27.7 (14.8)
Ouster | 4.9 (3.1) | 54.6 (36.8)
Virtual | 7.2 (4.9) | 38.6 (17.3)
* Aggregated results from 15 sequences across four sessions, with durations of 4-10 min, trajectory lengths of 230-1050 m, and rotations of 1100-3000° ** Training data from 30 sequences from the same four sessions, with no overlap with sequences for evaluation
Mean and standard deviation of absolute orientation error (AOE, °) across 15 sequences
Mean and standard deviation of absolute position error (APE, m) across 15 sequences
matters
, matter
 | Without nODE | With nODE
TDK | 12,026.8 (6,156.1) | 22,734.0 (33,131.8)
Ouster | 6,327.2 (6,387.6) | 123,810.1 (151,618.9)
Virtual | 6,497.9 (3,465.0) | 10,157.8 (15,289.8)

## Slide 18
Where we are at
Calibration of IMUs
Multi-IMU fusion for noise & drift reduction
Learning-based IMU bias estimation
Mutiple-IMU experiments for wheel-IMU odometry
Wheel–IMU odometry with individual IMUs (TDK, Ouster, Virtual)
Wheel–IMU odometry with multiple IMUs
When integrated into Gluon codebase

## Slide 19
Wheel–IMU odometry with individual IMUs (TDK, Ouster, Virtual)
Using a virtual IMU for wheel-IMU odometry yields lower errors than using either the TDK or Ouster IMU individually
2025-07-18-15-11-06
2025-07-23-13-59-33
Translation error in wheel–IMU odometry (/odom_fusion) over nine 1-hour sessions, depending on the IMU(s) used
IMU | Mean (Stdv.)
TDK | 0.324 (0.397)
Ouster | 0.600 (0.667)
Virtual | 0.292 (0.256)
TDK + Ouster | 0.263 (0.261)
TDK + Ouster + Virtual | 0.239 (0.180)

## Slide 20
Wheel–IMU odometry with multiple IMUs
2025-07-18-15-11-06
2025-07-23-13-59-33
Translation error in wheel–IMU odometry (/odom_fusion) over nine 1-hour sessions, depending on the IMU(s) used
Using multiple IMUs for wheel-IMU odometry yields lower errors than using a single IMU
TDK+Ouster+virtual yields lower errors than TDK+Ouster
What existing Gluon codebase does
IMU | Mean (Stdv.)
TDK | 0.324 (0.397)
Ouster | 0.600 (0.667)
Virtual | 0.292 (0.256)
TDK + Ouster | 0.263 (0.261)
TDK + Ouster + Virtual | 0.239 (0.180)

## Slide 21
Summary
In General (Theory, Literature, etc.) | For Drive Units
Calibration is beneficial | Calibration is beneficial
Combining multiple IMUs of a similar grade can reduce noise | Combining the TDK and Ouster IMUs may not reduce all white noise and random walk characteristics; however, using a virtual IMU improves wheel-IMU odometry when tested over multiple sessions on a drive unit
Neural ODE can estimate biases well on open-source datasets | Neural ODE does not estimate biases well on the drive unit; this requires further work

## Slide 22
Thank You!